## Slide 1
KNUST · COMPUTER SCIENCE · FINAL YEAR PROJECT 2026
DriveSense
Real-Time Driver Drowsiness & Distraction Detection
Webcam + MediaPipe + Random Forest. Detects AWAKE / DROWSY / YAWNING, head-pose distraction, gaze deviation, micro-sleep events, and computes a rolling fatigue score — served via a live Flask web dashboard.
AWAKE
DROWSY
YAWNING

## Slide 2
OBJECTIVE
Detecting fatigue and distraction before they become dangerous
The goal
Build a production-grade, real-time drowsiness and distraction detector that outperforms rule-based systems and persists detection data across sessions.
DriveSense uses MediaPipe facial landmarks and a Random Forest classifier to monitor driver alertness. A Flask dashboard streams live video, biometric charts, and a rolling fatigue score. Per-driver calibration profiles and SQLite event logging make it production-ready.
What DriveSense does
Capture and analyse webcam video at 25–30 FPS in real time
Extract 478 facial landmarks via MediaPipe Face Landmarker
Compute EAR, mouth ratio, iris ratios, and head-pose angles
Classify AWAKE / DROWSY / YAWNING; detect head-pose distraction, gaze deviation, blink anomalies, and micro-sleep
Persist events to SQLite and per-driver calibration to JSON profiles
Serve live MJPEG video + SSE biometric stream via Flask dashboard

## Slide 3
TOOLS & TECHNOLOGIES
Built with an open-source Python stack
Python
Core language — all pipeline modules
OpenCV
Webcam capture, frame annotation, MJPEG encoding
MediaPipe
478-point face landmark detection (face_landmarker.task)
NumPy / Math
EAR / mouth ratio / iris ratio geometry
Pandas
Dataset loading, feature inspection, temporal split
Flask
Web dashboard: MJPEG stream + SSE events + REST API
Scikit-learn
Random Forest training, temporal split, 5-fold CV
sounddevice
880 Hz alert tone — cross-platform audio output
Matplotlib
Confusion matrix + feature importance plots

## Slide 4
SYSTEM WORKFLOW
From webcam frame to alert, dashboard, and event log
01
Webcam
Capture frames via OpenCV VideoCapture
02
MediaPipe
Extract 478 landmarks + facial transform matrix
03
Feature Extraction
EAR, mouth ratio, iris H/V ratio, head pitch/yaw
04
ML Classifier
Random Forest → AWAKE / DROWSY / YAWNING
05
Rule Checks
Head-pose, gaze, blink rate, micro-sleep
06
Alert + Dashboard
880 Hz alert + MJPEG stream + SSE fatigue score

## Slide 5
STEP 2 · FACE LANDMARKS & FEATURE MODULE
MediaPipe maps 478 points; features.py extracts all ratios
The shared module src/features.py defines landmark index groups and computes EAR, mouth ratio, and iris ratios. Importing from this one module eliminates train/serve skew — training and inference always use identical feature logic.
Left eye: landmarks [33, 160, 158, 133, 153, 144]
Right eye: landmarks [362, 385, 387, 263, 373, 380]
Iris centres: 468 (left), 473 (right) for gaze tracking
EYES → EAR + Iris H/V Ratio
MOUTH → Mouth Open Ratio

## Slide 6
STEP 3 · FEATURE EXTRACTION
Four computed features per frame
Eye Aspect Ratio (EAR)
Measures eye openness. Low EAR = closed / drowsy. Threshold: 0.40.
EAR = (v1 + v2) ÷ (2 × h)
v1, v2 = vertical distances · h = horizontal span (6 landmarks)
Adjustable per driver via calibration — persisted to profiles.
Mouth Open Ratio + Iris Ratios
Yawning: mouth ratio > 0.10. Gaze: iris_h_ratio and iris_v_ratio.
Ratio = vertical ÷ horizontal
Iris H: 0.0=left 0.5=centre 1.0=right
Iris V: 0.0=up 0.5=centre 1.0=down

## Slide 7
STEP 4 · MULTI-MODAL DISTRACTION DETECTION
Head-pose, gaze, blink rate, and micro-sleep checks
Detection rules
Head-pose |pitch| > 20° or |yaw| > 25°
≥ 15 frames
Iris H ratio < 0.28 or > 0.72
≥ 20 frames
Micro-sleep: eye closure 3–15 consecutive frames
≥ 3 events / 60 s
Blink rate anomaly (60 s sliding window)
Monitored
Rule checks run every frame alongside the ML classifier. If any rule fires, the ML label is overridden with DISTRACTED or MICRO-SLEEP!
Priority order
DISTRACTED
|pitch|>20° or |yaw|>25° for 15+ frames — fires first
MICRO-SLEEP!
3+ micro-sleep events in 60 s — fires second
AWAKE
ML label (AWAKE / DROWSY / YAWNING) if no rule fires

## Slide 8
STEPS 5–6 · DATASET & TEMPORAL SPLIT
4,742 labelled frames — split by time, not randomly
save_dataset.py → data/drowsiness_dataset.csv (4,742 rows)
›
timestamp
›
left_ear
›
right_ear
›
avg_ear
›
mouth_ratio
›
closed_eye_frames
›
open_mouth_frames
›
status
← class label
Temporal split: first 80% train, last 20% test (not random)
AWAKE
Normal, alert facial state (majority class)
DROWSY
Eyes closed / heavy eyes — simulated fatigue
YAWNING
Wide sustained mouth open — simulated yawn
check_dataset.py
Why temporal? closed_eye_frames is a sequential counter. Adjacent frames share near-identical values, so a random split leaks data between sets, inflating accuracy.

## Slide 9
STEP 7 · MODEL TRAINING
RandomForestClassifier — n_estimators=100
Six numeric features → AWAKE / DROWSY / YAWNING
left_ear
right_ear
avg_ear
mouth_ratio
closed_eye_frames
open_mouth_frames
Why Random Forest?
Handles EAR/mouth numerical features, runs at real-time speed on CPU (no GPU). Feature importance rankings available. NO-FACE rows stripped before fit. Model saved via joblib to models_ml/drowsiness_model.pkl.
Temporal split
Chart: 
| Training | Testing
Split | 80 | 20
80 / 20

## Slide 10
STEP 8 · LIVE INFERENCE — TWO MODES
Terminal (OpenCV) + Web Dashboard (Flask)
python src/app.py → http://127.0.0.1:5001
1
Background thread reads webcam frames
2
MediaPipe extracts 478 landmarks per frame
3
features.py computes EAR, mouth, iris ratios
4
ML classifier + head-pose + gaze + micro-sleep
5
Annotated frames → MJPEG stream at /video_feed
6
State + fatigue score → SSE stream at /events
DASHBOARD OUTPUT
Status: AWAKE / DROWSY / DISTRACTED
Fatigue Score: 0–100 (rolling 5 min)
Chart.js EAR timeline + event log

## Slide 11
STEP 9 · EVALUATION RESULTS
99.6% hold-out accuracy — ML crushes rule-based
evaluate_model.py + compare_models.py → results/
Hold-out Accuracy
99.6% (759 frames, temporal test set)
5-Fold CV
97.9% ± 2.2% (range 94.3–99.9%)
Rule-Based Accuracy
50.1% — 0% DROWSY recall
ML DROWSY F1
1.00 (perfect precision + recall)
Key finding
The Random Forest achieves 100% DROWSY recall vs 0% for the rule-based system. Temporal split is essential — random splitting inflates accuracy to ~100% artificially by leaking sequential frame counters.
Temporal split prevents leakage

## Slide 12
PERSISTENCE LAYER
Event logging, driver profiles & fatigue score
Chart: 
| DISTRACTED | YAWNING | DROWSY | MICRO-SLEEP!
Fatigue Points Added | 2 | 3 | 10 | 15
FATIGUE SCORE
0–100
rolling 5 min
db.py logs events to data/events.db (SQLite). profiles.py saves calibrated EAR thresholds to data/profiles/{name}.json — restored on driver switch. Fatigue weights: DROWSY +10, MICRO-SLEEP +15, YAWNING +3, DISTRACTED +2. Broadcast in every SSE update at /events.

## Slide 13
LIMITATIONS & CONCLUSION
DriveSense — production-ready, with room to grow
Known limitations
—
Sensitive to lighting — MediaPipe needs adequate illumination
—
Single-subject training dataset — may not generalise without retraining
—
No real vehicle validation — stationary simulation only
—
Dashboard fatigue gauge widget not yet wired in index.html
—
Night-vision / IR camera support not yet implemented
In conclusion
DriveSense achieves 99.6% hold-out accuracy with a Random Forest trained on 4,742 frames (temporal split). Multi-modal coverage: head-pose distraction, gaze deviation, micro-sleep, per-driver calibration, SQLite event persistence, and a rolling fatigue score.
The Flask web dashboard streams live MJPEG video and SSE biometric data to any browser — no app install required. The system classifies the driver as:
AWAKE
DROWSY
YAWNING

## Slide 14
FUTURE WORK
DriveSense — from desktop prototype to in-vehicle deployment
Path to in-car deployment
—
Edge hardware — Raspberry Pi 5 / Jetson Nano, dash- or column-mounted
—
Headless operation — systemd service, auto-starts on boot
—
Configurable camera source — replace hardcoded cv2.VideoCapture(0)
—
Vehicle power — 12V accessory socket via buck converter
—
Real vehicle validation — vibration, lighting, genuine fatigue
Beyond the prototype
The current build is a desktop app: laptop and webcam. That proves the detection pipeline works, but a real driver-monitoring system needs to run unattended in a moving vehicle, not tethered to a laptop on the dash.
The web dashboard becomes a post-drive review and fleet-monitoring tool. In the vehicle, the audible alert stays the primary driver-facing output. Target hardware:
PI 5
JETSON
12V